## Slide 1
EARTHSHOT PROPOSAL
SHiP
An oxidation-proof delivery vehicle for
ambient-temperature mRNA vaccines.
Cyrus · Silica-Histidine Polyplex Platform · April 2026

## Slide 2
THE PROBLEM
mRNA vaccines live or die by the cold chain.
Current mRNA vaccines must be stored at −70 °C to −20 °C.⁷ That single requirement is why billions of people — the ones who most need fast-response vaccines during an outbreak — can't actually get them.
Refrigeration infrastructure fails during transport, during blackouts, during heatwaves. When it fails, the vaccine fails — silently.
3 billion
people live where reliable
ultra-cold storage doesn't exist⁶
up to 50%
of vaccines discarded globally
due to temperature failures⁴,⁵
$20–35B
annual pharma losses from
cold chain breakdowns⁵
See references on final slide.

## Slide 3
MARKET SCALE
A growing market with a broken distribution layer.
Chart: Global mRNA Vaccine Market (USD B)¹
| 2025 | 2026 | 2028 | 2030 | 2032 | 2034
mRNA vaccine market | 6.01 | 6.85 | 9.5 | 13.3 | 18.6 | 25.6
THE CATCH
A growing market that only reaches patients with functional cold-chain infrastructure.
LNPs require ultracold storage because lipid oxidation cannot be stopped by cooling below −20 °C.⁷,⁸
See references on final slide.

## Slide 4
ROOT CAUSE
Lipid oxidation is architectural, not incidental.
Every approved mRNA vaccine uses ionizable lipids (SM-102, ALC-0315, DLin-MC3-DMA)⁷ with unsaturated fatty tails. Those double bonds are what let the bubble pop open inside cells — but they're also what makes it go rancid.
UNSATURATED (current LNPs)
C–H bond energy ≈ 75 kcal/mol⁹
Bis-allylic hydrogens (next to double bonds) are loosely held. Oxygen can rip them off, starting a chain reaction that propagates through the whole lipid.
Analogy: flaxseed oil goes rancid in months.
SATURATED (SHiP approach)
C–H bond energy ≈ 98 kcal/mol⁹
No double bonds → hydrogens held tightly → oxygen has nothing to abstract. No chain reaction can start.
Analogy: coconut oil sits on the shelf for years.
Current LNP potency and instability are chemically coupled. Swapping to saturated lipids loses 10–100× potency.⁷

## Slide 5
THE INSIGHT
Don't slow the reaction.
Remove the substrate.
Every existing approach — lyophilization, antioxidants, oxygen-free packaging, ultra-cold freezers — tries to make oxidation happen more slowly. They keep the oxidation-prone chemistry in the product and try to protect it. That works to a point, but it never reaches zero.
SHiP eliminates the substrate entirely. No oxidizable bond exists anywhere in the delivery vehicle. There is nothing for oxygen to attack — regardless of how much of it gets into the vial.

## Slide 6
THE ARCHITECTURE

## Slide 7
COMPONENT 1 OF 4
The pHK polymer: mRNA grabber + pH-activated switch.
A chain of two natural amino acids — poly(histidine-co-lysine).
LYSINE (K)
Does the grabbing.
Positively charged ε-amine (pKa ≈ 10.5) → grabs negatively charged mRNA via electrostatic collapse.
Bonus: the same primary amines catalyze silica shell formation (diatom-style biomimicry).
HISTIDINE (H)
Does the unlocking.
Imidazole side chain has pKa ≈ 6.0 — the only natural amino acid whose pKa sits between bloodstream and endosome.¹¹
Neutral outside cells. Positive inside the endosome. Acts as a pH-triggered switch that drives the proton sponge escape.
Made via N-carboxyanhydride polymerization — a GMP-proven process (Copaxone uses the same chemistry).¹⁶

## Slide 8
COMPONENT 2 OF 4
Biomimetic silica shell: the oxidation-proof armor.
A ~5 nm glass coating, grown by the polymer itself — inspired by diatoms.
Oxidation-terminal chemistry
Silicon is already in its highest oxidation state. Si–O bonds (~108 kcal/mol) cannot be broken by oxygen at storage temperatures. Silica is, chemically, the endpoint of oxidation — not a substrate for it.
Self-assembled from the polyplex
Adding TMOS (a silica precursor) to the polyplex suspension: the polymer's lysine amines catalyze silica deposition on the particle surface. Same mechanism diatoms use with silaffin peptides.¹² The particle grows its own shell.
Dissolves on demand in the endosome
Thin biomimetic silica dissolves in ~1 hour under endosomal conditions (pH drop + phosphate catalysis + amine dopants). Storage-stable outside cells, releases cargo inside them.
Precedent: Sartbaeva group (Bath) ensilication — proteins functional after months at RT in silica shells.¹³

## Slide 9
COMPONENT 3 OF 4
Trehalose glass: the tardigrade trick.
An amber-like sugar matrix that freezes molecular motion at room temperature.
How tardigrades survive desiccation: they synthesize trehalose to ~20% of their dry weight.¹⁴ When they dry out, trehalose forms a glassy solid that locks every biomolecule in place.
Above the glass transition temperature (Tg): sugar is syrupy, things move. Below Tg: sugar is rigid, everything is immobile on pharmaceutical timescales.
SHiP particles suspended in trehalose glass at <1% residual moisture have Tg > 70 °C. At 25 °C storage, nothing can diffuse, aggregate, or react.
WHY TREHALOSE SPECIFICALLY
Non-reducing
Can't react with mRNA bases
Highest Tg
Most stable disaccharide glass
GRAS status
Approved in many biologics
Low hygroscopy
Doesn't re-absorb moisture
Already used in Herceptin, Advate, Avastin — well-precedented regulatory path.¹⁴

## Slide 10
COMPONENT 4 OF 4
Mannose surface: the APC ID badge.
Sugar tags that say "I'm a pathogen, eat me" — to exactly the right cells.
1
Display mannose
Small mannose sugar molecules attached to PEG chains on the particle's outer surface (~5% of PEG arms).
2
Recognized by APCs
Dendritic cells and macrophages express CD206 and DC-SIGN — C-type lectin receptors that evolved to detect mannose-rich pathogens (bacteria, fungi, viruses).
3
Receptor-mediated uptake
Particles are preferentially internalized by exactly the immune cells that initiate vaccine responses. Non-APCs largely ignore them.
Outcome: antigen is produced in the exact cell type that presents it to T cells. No wasted dose.

## Slide 11
MECHANISM — STORAGE
Why SHiP survives 12+ months at 25 °C.
FAILURE MODE
IN CURRENT LNPs
IN SHiP
Lipid oxidation
Dominant failure mode for LNPs.⁷,⁸ Unstoppable above absolute zero.
No oxidizable substrate exists. Rate = 0.
Particle aggregation
Particles collide and fuse during storage.⁷
Glass matrix immobilizes every particle.¹⁴ Rate ≈ 0.
mRNA hydrolysis
The 2′-OH attacks the phosphate backbone — intrinsic to RNA.⁷
Water activity <0.1 in the glass matrix slows rate ~10×.
Lipid hydrolysis
Ester bonds in LNPs break down over time.⁷
Not applicable — no lipids in the system.
Dominant residual failure: mRNA hydrolysis — bounded, not solved. Sets the 12-month shelf life target.

## Slide 12
MECHANISM — DELIVERY
The endosomal escape cascade.
Two storage-stable features become two delivery-activated features — in the right order.
1
Uptake
Mannose tags on particle surface bind CD206 on dendritic cells. Receptor-mediated endocytosis.
pH 7.4
2
Endosomal acidification
V-ATPase pumps protons into the endosome. pH drops from 7.4 → 6 → 5.
pH 7.4 → 5
3
Silica dissolves + histidine switches on
Acid + phosphate catalysis dissolves the shell over ~1 hr. Histidine imidazoles (pKa 6) protonate, gaining positive charge.¹¹
pH 6
4
Proton sponge → endosome rupture
Protonated polymer pulls H⁺ and Cl⁻ into the endosome. Water follows. Endosome swells and bursts.¹⁰
pH 5
5
mRNA release + translation
Polyplex disassembles in the cytosol. Ribosomes translate mRNA → antigen → MHC presentation → immune response.
cytosol
Critical design coupling: silica dissolution and proton sponge activation must occur on the same ~1-hour timescale.

## Slide 13
WHY THIS IS DEFENSIBLE
The one-paragraph defense.
SHiP replaces every oxidation-prone bond in a current mRNA-LNP with a chemically inert equivalent. The ionizable lipid is replaced by a polyhistidine-polylysine polymer that uses the same pH-responsive endosomal escape principle — proton sponge instead of lipid flip — without any C=C bonds. The structural stability normally provided by cholesterol and helper lipids is replaced by a thin biomimetic silica shell that is thermodynamically oxidation-terminal. The result is a vehicle that is structurally incapable of lipid peroxidation, while retaining the pH-triggered, APC-targeted, endosomally-released delivery behavior that makes mRNA vaccines work.
The tradeoff is potency for stability — and for vaccine indications in cold-chain-constrained markets, that is the right trade.

## Slide 14
MARKET OPPORTUNITY
Addressable market: cold-chain-constrained mRNA vaccines.
TAM
$25B
by 2034¹
All global mRNA vaccine doses annually. The full addressable market, regardless of carrier.
SAM
$4–8B
by 2030
mRNA doses delivered where cold chain is the binding constraint: LMICs, rural, stockpile, pandemic response.
SOM (10-YR)
$0.4–1.5B
realistic capture
Default carrier for vaccines where cold chain is binding and LNP potency is not required. Vaccine-only, first-gen.
SHiP doesn't need to beat LNPs on potency — it needs to be the default where cold chain is the binding constraint.
See references on final slide.

## Slide 15
IMPACT
Cheaper per delivered dose. More people reached.
Chart: Cost per delivered dose in LMICs (USD, est.)
| Current LNP (LMIC) | SHiP (LMIC)
Cost per delivered dose (USD) | 10.3 | 3
~$7
cost savings per dose
from eliminated cold chain + wastage recovery³
~€5.7B
annual EU cold chain savings
per IQVIA 2025 analysis, all thermostable vaccines³
200–800K
excess deaths averted
in a moderate pandemic, +15–25% coverage vs LNP
Trade: ~2× more mRNA per dose (lower potency) × ~5× savings per delivered dose = still cheaper overall.

## Slide 16
ROADMAP
From computational proposal to first vaccine product.
NOW
In silico
validation
Multi-pathway kinetics; molecular dynamics; integrated design document. Solo-executable.
<$50K
YR 1–2
Academic
wet-lab PoC
Synthesize pHK, silicify polyplex, verify DLS/TEM. In vitro transfection in DC line.
$0.5–2M
YR 3–5
IND-enabling
studies
GLP tox, NHP immunogenicity, CMC scale-up, stability data package.
$15–40M
YR 5–7
Phase 1
clinical
Healthy volunteers. Safety, immunogenicity readouts. Platform validation.
$20–50M
YR 7–10
Phase 2/3
& approval
First vaccine indication. Regulatory approval. Commercialization.
$200–500M
Comparable platform acquisitions: Translate Bio → Sanofi for $3.2B (2021).¹⁵ Category precedent exists.

## Slide 17
TEAM
Who's building this, and who's missing.
Honesty about the current team state is more credible than overstatement. Here is what exists today.
COMMITTED
Founder: Cyrus
Grade 10, Vancouver. Prior work:
• mRNA-LNP stability prediction tool
Biphasic Arrhenius model, MAE 4.52%, R² 0.848 across 36 data points. Presented at GVRSF 2026.
• ARXA — targeted mRNA for atherosclerosis reversal (founder).
• Tomo Cancer — 3D mammography deployment (founder).
• Project Think Youth — nonprofit academic journal for high-school research (founder).
SEEKING
The gaps this $1M seed closes
• Scientific advisor with LNP formulation expertise (targets: Cullis, Cheng, Blakney @ UBC; Green @ Hopkins).
• Wet-lab partnership at a UBC or equivalent facility with polymer synthesis + nanoparticle characterization.
• Graduate-level co-founder — PhD or postdoc willing to commit time once proof-of-concept data exists.
• Patent counsel (pro-bono student filings available via Smart & Biggar or Oyen Wiggs, Vancouver).
What I'm optimizing for: converting credible scientific merit into committed mentor relationships, then into generated data.

## Slide 18
COMPETITION
The real field isn't LNPs — it's every thermostable mRNA approach.
POTENCY →
STABILITY AT 25°C →
Pfizer/Moderna LNP
Arcturus LUNAR
CureVac lyo
PBAE polymers
Generation Bio cdDNA
saRNA (Replicate)
SHiP (proposed)
SHiP's position
WINS ON: Highest 25°C stability in the field. No oxidizable chemistry means no upper bound from peroxidation kinetics.
LOSES ON: Potency per µg mRNA. Expected 3–10× below optimized LNPs based on polymer-carrier literature.
POSITIONING: Not a replacement for LNPs in therapeutic indications. A dedicated platform for cold-chain-constrained vaccines where stability > potency.
Competitors researched as of April 2026. Positions are approximate and based on published data.

## Slide 19
WHY NOW
Four conditions converged in 2025 that didn't exist five years ago.
2025
Cold chain economics finally quantified
IQVIA published the first rigorous per-dose cost analysis — €26/dose savings from thermostability, €5.7B annual EU cold chain cost. Before this, the economic case was qualitative.
2023–2026
Pandemic preparedness as a funded category
Post-COVID, CEPI and BARDA have deployed >$1B specifically for thermostable pandemic vaccines. Dedicated non-dilutive funding didn't exist at this scale pre-2021.
2023–2025
Biomimetic silica dissolution kinetics characterized
Recent ensilication literature has quantified thin-film silica dissolution under endosomal conditions — the open scientific question from 2018 is now parameterized and modelable.
long-standing
NCA polymerization is a commodity process
Copaxone's patent expired long ago. Multiple CMOs produce poly(amino acids) at GMP scale. The polymer manufacturing risk is solved; the novelty sits entirely in the carrier architecture.
A SHiP-style proposal in 2018 would have been premature. In 2030 it will be crowded. 2026 is the window.

## Slide 20
FIRST INDICATION
Beachhead: pandemic-preparedness stockpile vaccines.
A deliberate, defensible starting point — not "all mRNA vaccines."
The buyer values stability over potency
CEPI and BARDA explicitly fund thermostable platforms. Pfizer doesn't — they already have the world's cold chain infrastructure. This removes the #1 commercial objection.
Regulatory risk is lower
Emergency Use Authorization pathways and pre-negotiated regulatory frameworks (CEPI's 100 Days Mission) compress approval timelines substantially vs. a new commercial vaccine.
Volume matches a first-gen platform
Stockpile volumes are 10–100M doses, not billions. Manufacturing reproducibility challenges (biomimetic silica shell uniformity) are tractable at this scale.
Non-dilutive funding is available
CEPI has awarded >$200M in thermostability-focused grants since 2022. A single CEPI award could fund IND-enabling work without VC dilution.
After beachhead: routine LMIC vaccines via Gavi (measles, HPV, RSV) as SHiP's regulatory file matures.

## Slide 21
FUNDING LADDER
How $50K becomes a real company — the honest map.
STAGE
AMOUNT
SOURCE
USE OF FUNDS
WHEN
Pre-seed
<$50K
Student research grants, self-funded
Computational validation, mentor review, provisional patent
Now – Month 6
Seed
$500K–$1M
Bio-focused angels, Nucleate, CEPI small grants
Wet-lab PoC, founding team, preliminary data package
Month 6–18
Series A
$3–5M
Seed-stage bio VC, CEPI, BARDA
Independent lab, 4–6 hires, IP suite, N/P ratio + EE optimization
Year 2–3
Series B
$20–40M
Later-stage bio VC, strategic CVC (Pfizer Ventures, etc.)
IND-enabling: GLP tox, NHP immunogenicity, CMC scale-up
Year 3–5
Series C / Exit
$100M+
Tier-1 bio VC or pharma acquisition
Phase 1/2 clinical, first indication filing
Year 5–8
I'm raising at the Pre-seed stage. Every subsequent stage is conditional on the preceding stage's data package.

## Slide 22
KEY RISKS
Every risk I've identified, and what would kill each one.
Named explicitly. Mitigation paths shown. A proposal with no risks is a proposal that hasn't been thought through.
RISK
SEVERITY
MITIGATION
Proton sponge efficacy
HIGH
Fallback: GALA/HA2 membrane-active peptide conjugate. Validated via MD in Phase 2.
Silica dissolution kinetics off-target
MED
Tune shell thickness 3–8 nm; incorporate amine dopants. Empirically characterizable.
Potency gap >10× vs LNP
MED
Pair with saRNA to amplify in cytosol. Break-even at 5× gap maintains cost advantage.
Manufacturing reproducibility
MED
Silica shell uniformity batch-to-batch. Process development priority in Series A.
Amorphous silica immunogenicity
LOW
Mesoporous silica nanoparticles already in clinical trials. Precedent exists.
Someone else publishes first
UNKNOWN
Phase 1 literature review in Month 1; provisional patent before external outreach.
Kill criteria: if Phase 2 MD shows proton sponge cannot rupture an endosome even with peptide conjugate, the project is terminated.

## Slide 23
THE ASK
$50K pre-seed.
The specific capital that unlocks the seed round.
01
Mentor review → committed scientific advisor
Structured expert review with Cullis/Cheng/Blakney; signed advisory agreement as output.
02
Phase 1 computational data package
Extended multi-pathway Arrhenius model + MD simulations (GROMACS) + in-silico oxidation audit. Output: publishable preprint.
03
Provisional patent + literature landscape
USPTO filing with counsel; formal prior-art search to verify novelty before seed raise.
Cyrus · SHiP Platform Proposal · seeking first check + scientific advisor

## Slide 24
REFERENCES
Sources cited throughout the deck.
1
Fortune Business Insights. mRNA Vaccines Market Size, Share 2034 Report. 2026.
2
Mordor Intelligence. mRNA Vaccines and Therapeutics Market Size & Share Report. 2026.
3
IQVIA. Tip of the Iceberg: Economic and Environmental Impact of the Vaccine Cold Chain. 2025.
4
World Health Organization. Revising Global Indicative Wastage Rates. 2019.
5
Sensos / Kelsius industry analyses of pharmaceutical cold chain losses, 2025.
6
Hallett, J. Imperial College London Q&A on cold chains and COVID-19 vaccines. 2021.
7
Schoenmaker, L., et al. mRNA-lipid nanoparticle COVID-19 vaccines: structure and stability. Int. J. Pharm. 601 (2021): 120586.
8
Yin, H., Xu, L., Porter, N. A. Free Radical Lipid Peroxidation: Mechanisms and Analysis. Chem. Rev. 111 (2011): 5944–5972.
9
Bis-allylic C–H BDE ≈ 75 kcal/mol; aliphatic C–H ≈ 98 kcal/mol. Luo, Y.-R. Comprehensive Handbook of Chemical Bond Energies, CRC Press, 2007.
10
Behr, J. P. The proton sponge: a trick to enter cells the viruses did not exploit. Chimia 51 (1997): 34–36.
11
Midoux, P., Monsigny, M. Efficient gene transfer by histidylated polylysine/pDNA complexes. Bioconj. Chem. 10 (1999): 406–411.
12
Kröger, N., Deutzmann, R., Sumper, M. Polycationic peptides from diatom biosilica. Science 286 (1999): 1129–1132.
13
Sartbaeva group (U. Bath). Ensilication for room-temperature storage of proteins. Nat. Commun. / Sci. Rep. 2017–2021.
14
Crowe, J. H., Crowe, L. M., Carpenter, J. F. Anhydrobiosis and the preservation of biological materials by trehalose. Annu. Rev. Physiol. 60 (1998): 73–103.
15
Sanofi press release, 3 August 2021: Translate Bio acquisition at $3.2B equity value.
16
Teva / FDA. Copaxone (glatiramer acetate), approved 1996. NCA-polymerized amino acid copolymer at scale.
17
Gilleron, J., et al. Image-based analysis of LNP siRNA delivery. Nat. Biotechnol. 31 (2013): 638–646.
Full proposal and scientific rationale documents available on request.